## Slide 1: Methodical Approach for Analyzing Process Variables and Optimizing Boundary Conditions in Multi-Axis Robot Programs
Submitted by: Jan Nalivaika Supervised by:
Garching 04.03.2024
Master-Thesis Presentation
Ludwig Siebert (TUM-iwb)
Marius Breuer (Siemens AG)
Notes: Ladies and gentlemen, thank you very much for joining my master thesis presentation with the title "Methodical Approach for Analyzing Process Variables and Optimizing Boundary Conditions in Multi-Axis Robot Programs." Before we jump in, I would like to explicitly thank my two supervisors, Ludwig Siebert and Marius Breuer. Without them, this work would not be possible.

## Slide 2: Table of Contents
Implementation and Results
5
Methodology
4
State of the Art
3
Problem Formulation and Aim
2
Motivation
1
Summary and Outlook
6
Notes: In the next few minutes, I will discuss the motivation for this topic, the problem formulation, and highlight the existing research gap in the current state of the art. Furthermore, we will dive into the methodology, implementation, and the obtained results. Finally, I will provide a summary and outlook. Following that, we can discuss any remaining questions.

## Slide 3: Growth of Industrial Robots and Applications
Motivation
400,000
350,000
300,000
250,000
200,000
250,000
100,000
50,000
0
[1] Hwa Jung and Dong-Geon Lim 2020
[2] Jiangnan Ni and Vipin Balyan 2021
2001 2002 2003 2004 2005 2006 2007 2008 2009 2010 2011 2012 2013 2014 2015 2016 2017
1,600
1400
1200
1000
800
600
400
200
0
(units)
(units)
Annual shipments of industrial robots (left axis)
Annual shipments of industrial robots per employee in manufacturing (right axis)
Growth of industrial robots
1) Automobile 2) Electrical/Electronic
3) Metal 4) Chemical 4) Food and Beverage 5) Pharmaceutical
6) Other
39.15%
19.85%
9.4%
19.85%
6.2%
1.2%
3.5%
Industrial applications sectors
[1]
[2]
Notes: When we look at the annual shipment of industrial robots, we see a significant growth over the last 15 years. In 2010, there were only 100,000 industrial robots shipped, but by 2017, this number had increased to almost 400,000. This growth indicates the increasing importance of industrial robots in the manufacturing industry. Not only are the absolute numbers of industrial robots increasing, but the ratio of robots to employees is also steadily rising. This suggests that industrial robots being increasingly adopted by companies to enhance productivity and efficiency. If we examine the areas of application, we find that the largest sector for robotic applications is the automobile industry, followed by the electrical and machinery industries. This indicates that industrial robots are being extensively utilized in these sectors to automate tasks and improve production processes. Overall, the growth in the shipment and their diverse applications highlight their increasing importance and impact in the manufacturing sector.

## Slide 4: Manufacturing Methods
Motivation
Designed for milling
High precision
Toolpaths in 5 DoFs
X, Y, Z (translation)
A, B (rotation)
5-DoF toolpath does not fully specify the robots’ configuration
Only X, Y, Z, A and B are defined
Rotation C is not specified and can be chosen freely
Rotation C is affecting how a toolpath is traversed
Rotation C is considered a boundary condition
6 DoFs
Used for WAAM
Can be used for milling
Highly versatile
Sub-optimal stiffness
Redundancy in the system when performing a 5-DoF task in a 6-DoF system
How does the boundary condition affect the robot?
Goal: Optimizing the robots' behavior by optimally setting the boundary condition
CNC: Computer numerical control; DoF: Degree of freedom WAAM: Wire Arc Additive Manufacturing
CNC machines
Industrial robots
Milling with robots
Influence of boundary condition
Notes: Even though the number of robots in the manufacturing industry is steadily increasing, traditional manufacturing still heavily relies on CNC machines. CNC machines, which stands for computer numerically controlled machines, are specifically designed for milling operations. They are known for high positional accuracy, which allows them to achieve repeatable precision on the um-scale. Most of the toolpaths executed on CNC mills are defined in 5 degrees of freedom. This means that the position of the endmill is defined by the coordinated X, Y, and Z axes, while the rotation is defined by the A and B axes. The rotation A and B represent the rotation of the tool around its X and Y axes respectively.
Industrial robots, in contrast, typically have 6 degrees of freedom, making them well-suited for pick and place or assembly operations. They excel in tasks that require flexibility and adaptability. One notable application of robots in manufacturing is their use in additive manufacturing processes, particularly in wire arc manufacturing. Additionally, robots can also be utilized for milling operations by attaching a spindle to the robot's flange, further showcasing their versatility. One potential disadvantage of industrial robots, when compared to CNC mills, is their lower stiffness. This can pose challenges when trying to produce parts with high precision.
The choice between using industrial robots or CNC mills depends on the specific requirements of the manufacturing process and the desired outcome.
It is possible to use the same toolpath designed for a CNC mill on an industrial robot. ???????????????????????
In the case of the robot, the rotation C, which represents the rotation around the TCP's Z-axis, is not defined in the toolpath. This rotation can be freely chosen and does not affect the toolpath itself. Regardless of the value of rotation C, the resulting part will be the same. However, the rotation C does affect how the robot behaves while traversing the toolpath and is considered a boundary condition in this example. The same principle applies to applications like Wire Arc Additive Manufacturing (WAAM) where the welding torch can be freely rotated. Regardless of the rotation of the torch, the resulting part will be identical. The rotation of the torch is not critical in terms of the resulting part geometry but may impact the behavior of the robot during the welding process.
Having one degree of freedom more than necessary results in redundancy. The question now is: How does the boundary condition affect the robot, and how can we use the redundancy to our advantage? The goal of this work is to optimize the robot's behavior by optimally setting the boundary condition.

## Slide 5: Example: Traversing a Toolpath With Different C-Rotation
Problem Formulation and Aim
Rotation C = 0°
Rotation C = -30°
Direction changes in the joints; Accelerations; Energy consumption; Cable positioning; Stiffness; etc.
Rotation C can be chosen freely
The rotation C significantly influences the behavior of the robot
Influenced process variables
Add video of robot here
Add video of NX here (if robot not available)
Add video of robot here
Add video of NX here (if robot not available)
THIS IS A VIDEO
THIS IS A VIDEO
Notes: The following two videos explain the problem visually.
On the left side, we see how the robot traverses a simple line in the negative y direction.
In this example, the rotations A, B, and C are all held at 0.
It is clearly visible that joint 4 has to rotate significantly to achieve the defined toolpath. On the right side, however, the rotation C is set to -30°.
It can be seen that the behavior of the robot is significantly different. The influenced process variables include:
- direction changes in the joints
- accelerations
- energy consumption
- cable positioning
- stiffness.

## Slide 6: Shortcomings in Current Methodologies
Problem Formulation and Aim
No currently published method allows the user to select specific process variables to evaluate a process
Provide a method that can work with specifically selected process variables and rate a manufacturing process
As of now, it is not possible to weigh individual process parameters and thus describe the manufacturing process as a singular scalar value
Extend the developed method with the option to add user-defined importance factor (weights) for the process variables
No available method provides a solution to optimize boundary conditions based on a user defined goal
Provide system that can optimize the boundary conditions while considering the user defined goal
Problem 1
Problem 2
Problem 3
Aim 1
Aim 2
Aim 3
Notes: After analyzing the current state of the art 3 problems became evident.
First of all:
No currently published method allows the user to select specific (user defined) process variables to evaluate a process.
Second:
As of now, it is not possible to weigh individual process parameters and thus describe the manufacturing process as a singular scalar value
Third: No available method provides a solution to optimize boundary conditions based on a user defined goal
The resulting Aim for the Thesis is:
First of all:
Provide a method that can work with specifically selected process variables and rate a manufacturing process
Second: Extend the developed method with the option to add user-defined importance factor (weights) for the process variables
For example, that
And lastly,
Provide system that can optimize the boundary conditions while considering the user defined goal

## Slide 7: Elaboration of the Research Gap
State of the Art
Stiffness
[11],[13],[14]
Velocity, Acceleration and Jerk
[8],[9],[10]
Energy Usage
[15],[16],[17]
Singularity Avoidance
[3],[4],[5],
[6],[7]
[3] Stevenson et al., (2002) [4] Bedrossian, (1990) [5] Huo and Baron (2008) [6] Milenkovic (2021) [7] Shi et al., (2021) [8] Dai et al., (2020) [9] Jiang et al., (2017) [10] Bien Duong (2021) [11] Wu et al., (2021) [12] Xiong et al., (2019) [13] Wang et al., (2022) [14] Cvitanic et al., (2020) [15] Uhlmann et al., (2016) [16] Boscariol et al., (2020) [17] Soori et al., (2015)
[12]
User defined process variables
User defined importance
factors
 marginal overlap in the publications
 no method takes a holistic approach
Research Gap
No possibility for the user to select process variables
No possibility for the user to weigh the individual process variables
No possibility to optimize the setting of redundant DoFs towards a user-defined goal
Missing elements
Notes: The current state of the art offers multiple publications for individual process variables.
For example, singularity avoidance, velocity, acceleration, and jerk, stiffness, or energy usage.
The main problem is that each publication is only focusing on the optimization of one process variable.
Only one publication covers three process variables simultaneously.
No publication is covering the option of user-defined process variables or user-defined importance factors.
The research gap results from the fact that there is only marginal overlap in the publications and no publication takes a holistic approach.
So the missing elements are:
A possibility for the user to select process variables
A possibility for the user to weigh the individual process variables
A possibility to optimize the setting of redundant DoFs towards a user-defined goal.

## Slide 8: Extraction of Process Variables
Methodology
Notes: In the developed methodology, the first step is to understand where the individual process variables can be extracted from.
For a given toolpath that must be traversed by the TCP, the inverse kinematic algorithm can give us the exact position of each joint.
These joint positions are in the form of a timeseries that specifies the rotational angle of the joint. Using these timeseries, it is possible to extract process parameters such as:
Direction changes in the joint
Total travel in the joints
Angular velocity, acceleration, and jerk With a forward kinematics approach, it is additionally possible to determine:
If all points of the toolpath are reachable
How close the robot is to a singularity
How the welding torch is oriented Further possible process variables include the continuous and total energy use.

## Slide 9: User Defined Importance Factors and Evaluation
Methodology
Selection of process variables
Selection of importance factors
Local rating calculation
Local score calculation
Global score calculation

## Slide 10: Boundary Condition Optimization
Methodology
Notes: Possible optimization algorithms:
  Evolutionary algorithm
  Genetic algorithms
  Particle swarm optimization
  Ant colony optimization
  Differential evolution
  Harmony search

## Slide 11: Modeled Robot and Analyzed Toolpath
Implementation and Results

## Slide 12: Traversing the Toolpath
Implementation and Results
THIS IS A VIDEO

## Slide 13: Extracting Joint Positions
Implementation and Results

## Slide 14: Local and Global Score
Implementation and Results

## Slide 15: Addition of a Second Redundant DoF in Form of a Rotary-Tilt-Table
Implementation and Results
Two redundant DoFs: 1) Rotation C (tool symmetry axis)
2) Tilting of the base-plate
THIS IS A VIDEO

## Slide 16: Visualization of the PSO-Algorithm
Implementation and Results
THIS IS A VIDEO
THIS IS A VIDEO
Notes: Make explanation sound good

## Slide 17: Valid Proof Of Concept
Summary and Outlook
A combination with CAM-software can significantly reduce computation time
Implementation of stiffness analysis to reduce chatter
Piecewise optimization of the toolpath instead of whole toolpath
The validation provides a solid proof-of-concept
Redundant DoFs can offer significant potential for improvement in the robot’s movement.
A PSO-algorithm is reasonable choice for finding the optimal boundary conditions
The method's adaptability allows for wide application to a broad spectrum of robotic systems
For a more detailed validation, longer production G-codes and multi-axis operations with more than two redundant DoFs are necessary
Outlook
Summary
Notes: The validation provides a solid proof-of-concept for the proposed methodology.
It is shown that the redundant DoFs can offer significant potential for improvement in the robot’s movement.
A PSO-algorithm is reasonable choice for finding the optimal boundary condition for two redundant DoF.
The method's adaptability allows for wide application to a broad spectrum of robotic systems
Additional factors need to be considered for detailed validation, such as longer production G-codes and complex multi-axis operations with more than two redundant DoFs.
A combination with CAM-software can significantly reduce computation time
Implementation of stiffens analysis
Piecewise optimization of the toolpath instead of whole toolpath

## Slide 18: Contact
THX
Jan Nalivaika
Student at Siemens
nalivaika@outlook.de
Ludwig Siebert
Supervisor at TUM
15578
ludwig.siebert@iwb.tum.de
Marius Breuer
Supervisor at Siemens
marius.breuer@siemens.com

## Slide 19: Sources
Ni and Balyan (2021) Research on Mobile User Interface for Robot Arm Remote Control in Industrial Application
Jung and Lim (2020) Industrial robots, employment growth, and labor cost: A simultaneous equation analysis
Stevenson et al., (2002) Singularity avoidance and aspect maintenance in redundant manipulators
Bedrossian,(1990) Classification of singular configurations for redundant manipulators
Huo and Baron, (2008) The joint‐limits and singularity avoidance in robotic welding
Milenkovic, (2021) Wrist singularity avoidance with a robot end-effector adding an oblique, redundant axis
Shi et al., (2021) Kinematics and Singularity Analysis of a 7-DOF Redundant Manipulator
Dai et al., (2020) Planning Jerk-Optimized Trajectory With Discrete Time Constraints for Redundant Robots
Jiang et al., (2017) Time-Jerk Optimal Trajectory Planning for a 7-DOF Redundant Robot Using the Sequential Quadratic Programming Method
Bien Duong (2021) On the Effect of the End-effector Point Trajectory on the Joint Jerk of the Redundant Manipulators
Wu et al., (2021) Review of Industrial Robot Stiffness Identification and Modelling
Xiong et al., (2019) Stiffness-based Pose Optimization of an Industrial Robot for Five-axis Milling
Wang et al., (2022) Optimization of redundant degree of freedom in robotic milling considering chatter stability
Cvitanic et al., (2020) Pose optimization in robotic machining using static and dynamic stiffness models
Uhlmann et al., (2016) Energy Efficient Usage of Industrial Robots for Machining Processes
Boscariol et al., (2020) Energy Optimization of Functionally Redundant Robots through Motion Design
Soori et al., (2015) Optimization of energy consumption in industrial robots, a review

## Slide 20: CNC machines

## Slide 21: Industrial Robot

## Slide 22: Manufacturing Systems with Redundant DoFs

## Slide 23: Singularity

## Slide 24: Interdependence of various parameters and elements

## Slide 25: Additional information for angular position of each joint

## Slide 26: Hard and soft limits with desired range

## Slide 27: Exemplary methods for energy usage calculations

## Slide 28: Rotation around the C-Axis of a welding torch

## Slide 29: Torch Orientation
Example of optimal and non-optimal tilt in the welding torch

## Slide 30: Transforming Time-Series Data into Scalar Values
Time-series data:
  Velocity
  Acceleration
  Jerk
  …
Optional procedures:
  Squaring and aggregation
  Cubing and aggregation
  Definition of thresholds
  Machine learning

## Slide 31: General Process Analysis

## Slide 32: Optimization Loop With CAM Software in the Loop

## Slide 33: Modeled Robot

## Slide 34: Modeling a Basic Toolpath

## Slide 35: Rotation around the Z-axis for toolpath 1

## Slide 36: Toolpath 2

## Slide 37: Toolpath 3

## Slide 38: G-code Variation

## Slide 39: Toolpath 2 and Score

## Slide 40: Toolpath 3 and Score

## Slide 42: Rotation toolpath 2

## Slide 43: Toolpath 3

## Slide 48
rotation around the Z-axis for toolpath 1

## Slide 50: Swarm Optimization